## Slide 1: ADALM PLUTO
Julio Tena
EE504
4/21/20

## Slide 2: ADALM PLUTO
Full Duplex
AD9363 Integrated RF Agile Transceiver
Fixed halfband decimation & interpolation filters and programmable 128-tap FIR filters
Source: Software-Defined Radio for Engineers

## Slide 3: ADALM PLUTO
Source: Software-Defined Radio for Engineers

## Slide 4: AD9363
Rx & Tx
  300 MHz – 3.8 GHz, 200 kHz – 20 MHz channel bandwidth, 65.1 kSPS – 61.440 MSPS
  2.4 Hz LO step size, 5 Hz sample rate step size
  12-bit DACs
* Frequency range can be configured to 70 MHz – 6 GHz
Source: Software-Defined Radio for Engineers

## Slide 5: AD9363
Rx & Tx
  300 MHz – 3.8 GHz, 200 kHz – 20 MHz channel bandwidth, 65.1 kSPS – 61.440 MSPS
  2.4 Hz LO step size, 5 Hz sample rate step size
  12-bit DACs
* Frequency range can be configured to 70 MHz – 6 GHz

## Slide 6: AD9363 - Rx
Signal acquisition
  LNA
    Splits off into two identical paths (IQ) components
    Provide analog gain
  Mixer (ZeroIF)
    Phase rotation of mixer’s clock
    Doubles effective bandwidth ( -fs/2, fs/2 )
  Filters
    Remove aliasing effects
    Maintain desired analog bandwidth
Source: Software-Defined Radio for Engineers

## Slide 7: AD9363 – Rx (continued)
  Digital Conversion
    ADC doesn’t provide all 12 bits (~ 4.5 bits of resolution)
    Additional bits gained in halfband filter (HBF) stages
    “Therefore, the best signal resolution is achieved through large oversampling of the input signal and then followed by several decimation stages”
Source: Software-Defined Radio for Engineers